## Slide 1: Junctional & Techinical

## Slide 2: Junctional Strips
Accelerated Junctional
Junctional Escape
Junctional Tachycardia
Premature Junctional Complex

## Slide 3: Accelerated
Rhythm, QRS, and Rate will be normal (60-100)
P Waves are either, hidden or after and if present will be inverted
PR I – Undeterminable

## Slide 4: Junctional Escape
Can happen in sinus arrest or PAC
Rhythm will be Regular, QRS Normal
Rate will be Brady 40-60
P Waves hidden, after, or inverted.
PRI Undeterminable.

## Slide 5: Junctional Tachycardia
Comes from Bundle of HIS
3+ PJC
Rate of > 100
Rhythm will be normal, QRS Normal
P Waves hidden, after, or inverted.
PRI Absent or short <.12

## Slide 6: Premature Junctional Complex
AV Site Fires spontaneous (Before SA)
Interrupts sinus
QRS Narrow (<.10sec)
P wave hidden, after, or inverted.
PRI Absent or short

## Slide 7: Technical

## Slide 8: Gain vs Speed
Gain
Standard = 1mm = 1mV
  5mm = .5mV
  10mm = 1.0mV
Speed
Standard Rate is 25mv/s
  1mm = 0.04 sec
  5mm = .20 sec
AKA Sweep Speed

## Slide 9: What if?
Complex's
Reduce gain
  Only if complex if off chart
Increase gain
  Only if complex is too little to read.
Rate
Increase speed. (Too fast)
  50mm/sec
Decrease speed (too slow)
  10mm/sec

## Slide 10: Interference
EKG machines are electronic, subject to interference.
  60 cycle interference
Muscle Tremors
  Somatic Tremor
Seizure Activity
Wi-Fi Single
  Cell Phone
Poor Connectivity