## Slide 1: Patient Vital Signs

## Slide 2: 4 Major Vitals
Blood Pressure
  Regular/Orthostatic
Pulse
Respirations
Sp02

## Slide 3: Blood Pressure
the pressure of the blood in the circulatory system, often measured for diagnosis since it is closely related to the force and rate of the heartbeat and the diameter and elasticity of the arterial walls
Systolic
  Systolic blood pressure (the upper number) — indicates how much pressure your blood is exerting against your artery walls when the heart beats
Diastolic
  Diastolic blood pressure (the lower number) — indicates how much pressure your blood is exerting against your artery walls while the heart is resting between beats.

## Slide 4: How to take
Locate Left Arm
  Closes to heart
Locate Median Cubital Artery
Apply Cuff
Pump Cuff to around 140mm/mg
  Check for sound
Start Releasing
  First beat is systolic number
  Last beat is diastolic

## Slide 5: Measurements *AHA standards
Blood Pressure Category | Systolic mm Hg (upper #) |  | Diastolic mm Hg (lower #)
Normal | less than 120 | and | less than 80
Prehypertension | 120 – 139 | or | 80 – 89
High Blood Pressure (Hypertension) Stage 1 | 140 – 159 | or | 90 – 99
High Blood Pressure (Hypertension) Stage 2 | 160 or higher | or | 100 or higher
Hypertensive Crisis (Emergency care needed) | Higher than 180 | or | Higher than 110

## Slide 6: Pulse
Related to heart beats
Should be taken for 30 seconds multiplied by 2
  If irregular pulse must be counted for 1 full minute
Sites
  Radial
  Femoral
  Brachial
  Carotid * Emergency*

## Slide 7: Pulse Values

## Slide 8: Respirations
Number of breaths
  Inhalation and Exhalation
Counted for 30 seconds
  Last 30 seconds of pulse check

## Slide 9: Sp02
Oxygen Saturation of Blood